## Slide 1: Smart Home
ITI – Summer Training Final Project

## Slide 2: Team Members
Mohamed Adel Mohamed Shalaby
Hazim Emad Ismail Mahmoud Ahmed

## Slide 3: Agenda
Introduction
1
Simulation
5
Microcontroller 2
3
Microcontroller 3
4
Microcontroller 1
2

## Slide 4
Introduction

## Slide 5: Introduction
This is a Smart Home project based on three atmega32 microcontrollers.
These microcontrollers communicate with each other using two different communication protocols, USART and SPI

## Slide 6: Introduction
This project supports the following features :
  User interface with keypad and LCD to take user choices
  Login system with the capability of changing password
  The user can control various smart systems and choose to enable or disable them
  These systems are Air Conditioner, Lights, Door and Music
  There is another automatic system which is Gas/Smoke detection with alarm
  Display all systems stats and the current temperature degree on another LCD

## Slide 7
Overview

## Slide 8: Introduction
APP
HAL
MCAL
RTOS
Microcontroller
Architecture

## Slide 9
Microcontroller 1

## Slide 10: Microcontroller 1
Login system
  User has 3 tries to enter the correct combination for the ID and password using the keypad.
  Each time the combination is incorrect, LCD 1 should display “Try Again!”.
  If all combination trials are exhausted, LCD 1 should display “Please Try Again Later!” , and the user is granted three more tries after 5 seconds.
  If the user manages to login, the user mode options should be displayed on LCD 1.

## Slide 11: Microcontroller 1
User Mode
  The user can choose from three things:
    Display options: shows all the configurable systems.
    Change pass: the user can update his/her password.
    Logout: user returns to the login screen.

## Slide 12: Microcontroller 1
Display Options:
  AC : allows the user to edit the threshold required to enable the fan system.
  LDR : allows the user to enable the automatic light system controlled by the LDR.
  DOOR : allows the user to open and close the door which consists of a servomotor.
  MUSIC : allows the user to enable the music system which is handled by the speaker and power/audio generator.
  RETURN : user goes back to the user mode screen.
Wrong user inputs are also handled.

## Slide 13: Microcontroller 1
Communication Protocols:
  Microcontroller one sends the user-edited data to and receives display data from Microcontroller two using USART.
  Data is sent as a register file with each control reserving a bit except for the temperature threshold which is sent alone.
  USART alternates between sending and receiving every 150ms to optimally run the code without noticeable delays.

## Slide 14: Microcontroller 1
Communication Protocols:
  Microcontroller one receives numbers entered on the keypad from Microcontroller 3 over SPI.
  SPI starts as soon as the user confirms the inputted number.
  The sent number is stored in a buffer until Microcontroller 1 receives it.
  Microcontroller 3 is the master while Microcontroller 1 is the slave in this process.

## Slide 15
Microcontroller 2

## Slide 16: Microcontroller 2
This microcontroller is responsible of all sensors data.
We used RTOS by implementing simple scheduler to handle different tasks.
Using USART protocol every 150ms :
  It sends sensors readings and systems stats to microcontroller 1
  It receives control signals from microcontroller 1 to control different modules like : (Door, Critical Temperature, Music and Lights).

## Slide 17: Microcontroller 2
Initialization
  Scheduler based on Timer 2 peripheral
  Input/Output pins direction for all sensors and devices
  USART protocol to communicate with microcontroller 1
  ADC peripheral to
    read temperature using LM35 sensor
    read light intensity using LDR sensor
  Timer 1 on Fast PWM mode to control the door motor

## Slide 18: Microcontroller 2
Scheduler Tasks :
  Communication with microcontroller 1
  Control Gas/Smoke System
  Control Air Conditioner System
  Control Lights System
  Control Door System
  Control Music System
Start the Scheduler
Scheduler Dispatcher in the main super loop to switch between tasks

## Slide 19: Microcontroller 2
Communication with microcontroller 1 :
  This task will be executed every 150ms
  It receives control signals from MC1 as follows :
    Critical temperature which controls the FAN
    Control LDR Signal
Turn On LDR System
Turn Off LDR System
1
0

## Slide 20: Microcontroller 2
    Control Door Signal
    Control Music Signal
Open The Door
Close The Door
1
0
Turn On Music System
Turn Off Music System
1
0

## Slide 21: Microcontroller 2
Communication with microcontroller 1 :
  It transmits systems stats like follows :
    Current Temperature Degree
    LDR System
LDR System is turned on
LDR System is turned off
1
0

## Slide 22: Microcontroller 2
    Door Status
    Music System
    Gas/Smoke Status
The Door is Opened
The Door is Closed
1
0
Music System is turned on
Music System is turned off
1
0
Gas/Smoke detected
No detection of Gas/Smoke
1
0

## Slide 23
Microcontroller 3

## Slide 24: Microcontroller 3
Keypad
  User interacts with the system using the keypad.
  User can type any number then press “#” to confirm that he/she has finished typing.
  User can delete a number by pressing the “*” button.

## Slide 25
Simulation

## Slide 28
Thanks